## Slide 1: Modeling SNS Availability Using BlockSim
Geoffrey Milanovich
Spallation Neutron Source

## Slide 2: Contributors
G. Dodson for providing initial reliability study and discussion
Vivian Chang (summer student from Carnegie Mellon) for building much of the accelerator reliability block diagram

## Slide 3: Outline
SNS Availability Numbers
Modeling an Entire Accelerator in BlockSim
Modeling Klystron End of Life Behavior

## Slide 4: Availability for Last 2 Runs
Chart: % available
| 40763.0 | 40770.0 | 40777.0 | 40784.0 | 40791.0 | 40798.0 | 40805.0 | 40812.0 | 40812.0 | 40819.0 | 40826.0 | 40833.0 | 40840.0 | 40847.0 | 40854.0 | 40861.0 | 40868.0 | 40875.0 | 40882.0 | 40889.0 | 40896.0 | 40903.0 | 40910.0 | 40917.0 | 40924.0 | 40931.0 | 40938.0 | 40945.0 | 40952.0 | 40959.0 | 40966.0 | 40973.0 | 40980.0 | 40987.0 | 40994.0 | 41001.0 | 41008.0 | 41015.0 | 41022.0 | 41029.0 | 41036.0 | 41043.0 | 41050.0 | 41057.0 | 41064.0 | 41071.0 | 41078.0 | 41085.0
Neutron Beam % Available | 0.94225 | 0.94877 | 0.96794 | 0.86429 | 0.87679 | 0.9519 | 0.97778 | 0.86935 | 0.90417 | 0.95857 | 0.95312 | 0.84426 | 0.92625 | 0.96989 | 0.89023 | 0.97627 | 0.95472 | 0.97922 | 0.9849 | 0.99615 | 0.97474 | 0.97222 | 0.96026 | 0.91594 | 0.98911 | 0.95737 | 0.93462 | 0.97754 | 0.85578 | 0.96183 | 0.95932 | 0.98544 | 0.98125 | 0.95417 | 0.87789 | 0.91127 | 0.75698 | 0.82381 | 0.98
Availability Goal
Run Running Avg. | 0.94225 | 0.94572 | 0.95241 | 0.93262 | 0.91975 | 0.92548 | 0.93219 | 0.92559 | 0.92559 | 0.92283 | 0.92672 | 0.92932 | 0.92338 | 0.92362 | 0.92719 | 0.92495 | 0.92757 | 0.92931 | 0.93232 | 0.93531 | 0.93587 | 0.97474 | 0.97347 | 0.96907 | 0.95699 | 0.9626 | 0.96167 | 0.95779 | 0.96009 | 0.95003 | 0.95132 | 0.95205 | 0.95466 | 0.95647 | 0.95628 | 0.95119 | 0.94883 | 0.93851 | 0.93118 | 0.93137
Commitment | 0.88 | 0.88 | 0.88 | 0.88 | 0.88 | 0.88 | 0.88 | 0.88 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9 | 0.9
FY running Avg. | 0.92008 | 0.92106 | 0.92232 | 0.92085 | 0.91942 | 0.92038 | 0.92176 | 0.92063 | 0.90417 | 0.93064 | 0.93803 | 0.91925 | 0.92071 | 0.92915 | 0.92427 | 0.92947 | 0.93247 | 0.93743 | 0.94198 | 0.94282 | 0.9455 | 0.94762 | 0.94854 | 0.94658 | 0.94884 | 0.94936 | 0.94855 | 0.94995 | 0.94598 | 0.94678 | 0.94734 | 0.94886 | 0.95003 | 0.95021 | 0.94755 | 0.94631 | 0.94026 | 0.93572 | 0.93582
FY12 Availability – 93.6%
Notes: FY average – 93.6%, run average 93.1%, commitment 90%

## Slide 5: FY 12 Downtime by Group
Chart: Hours down
| RF | E-HVCM | Ion Source | E-other | E-MagPS | Controls | Physics | Cryo | Beam Inst. | Prot. Sys. | Vacuum | CM/SRF | Cooling | RS/ESH | E-Choppers | Mech. | Ops | Target
FY12-1 | 24.2 | 7.7 | 12.3 | 10.6 | 11.4 | 4.4 | 9.1 | 11.2 | 4.7 | 2.5 | 2.6 | 0.7 | 0.2 | 0 | 0 | 0 | 0.1 | 0
FY12-2 | 73.3 | 65.2 | 21.6 | 10.6 | 7.4 | 9 | 2.9 | 0 | 5.2 | 4.3 | 2 | 3.6 | 2.8 | 1.8 | 1.7 | 1.1 | 1
FY11-3 before:
11-Nov-07
4-Mar
13-Mar
18-Nov-07
17-Apr
25-Nov-07
2-Dec-07
9-Dec-07
16-Dec-07

## Slide 6: Neutron Production Hrs, MWhrs, & Downtime by Year
Chart: Hours Delivered
| FY07 | FY08 | FY09 | FY10 | FY11 | FY12
Hrs. delivered | 2113.4 | 2806.6 | 3553.2 | 4249.7 | 5006.2 | 4092
MWh delivered to target | 158.5 | 944.6 | 2165.7 | 3456 | 4132 | 3750.8
Downtime | 1989.7 | 1494.1 | 1111 | 886.8 | 497.7 | 315.5
Availability | 66.8565 | 71.9844 | 80.7362 | 85.6449 | 92.1189 | 93.6406

## Slide 7: Downtime by Fiscal Year (07-12) Comparison
Presentation_name
Chart: System
| E-HVCM | Ion Source | RF | Target | E-MagPS | E-chopper | Controls | Vacuum | Cooling | E-other | Cryo | AP | Prot. Sys. | Misc./Mag/RS/ESH | BI | Fac./Mech. Sys. | Ops | Neut. Inst.
FY07 | 379.4 | 394.7 | 162.3 | 140.1 | 78.6 | 241.8 | 161.3 | 90.2 | 165.2 | 85.9 | 15.2 | 19 | 19 | 7.1 | 15.2 | 5.7 | 8.8 | 0.2
FY08 | 421.2 | 142.2 | 230.2 | 158.9 | 162.2 | 50.3 | 58 | 124 | 31.2 | 45.6 | 4.7 | 27.3 | 9.4 | 2 | 8.4 | 3.1 | 13.4 | 2
FY09 | 309 | 101.8 | 226.4 | 12 | 68.1 | 58.3 | 90.4 | 33.7 | 27.5 | 40 | 38.9 | 20.2 | 26.4 | 3.8 | 16.2 | 31.7 | 6.6 | 0
FY10 | 240 | 113.5 | 126.3 | 140.5 | 88.5 | 30.4 | 24.1 | 11.4 | 24.3 | 36.1 | 21.1 | 7 | 13.6 | 1.4 | 0.6 | 2.9 | 5.1 | 0
FY11 | 86.4 | 117.6 | 103.4 | 2.6 | 20.5 | 14.6 | 27.4 | 23.5 | 4.5 | 19.9 | 3 | 4.2 | 13.5 | 55.1 | 0.4 | 0.8 | 0.3 | 0
FY12 | 72.9 | 33.9 | 97.5 | 0.3 | 18.8 | 1.7 | 13.4 | 4.6 | 3 | 21.2 | 11.2 | 12 | 6.8 | 1.8 | 9.9 | 1.1 | 1.1 | 0

## Slide 8: Reliability Estimates, in the Beginning
“the spreadsheet” – numbers from industry, design specs, LANL, JLab, experts, and guesses
Exponential distributions only (constant failure rate)
For 160 hours mission time, availability:
  Source – 87%
  Linac – 80%
  Modulators – 99%
  Overall - ??
Notes: 160 hrs is 6.67 days, 20 shifts, 1 week

## Slide 9: RBD/BlockSim Advantages
Reliability Block Diagram (RBD) – “graphical representation of the components of the system and how they are reliability-wise related”
Many failure distributions allowed
Standby, load share, failure of switching to standby
Analytical solution of very complex diagrams (but not an accelerator)
Monte Carlo simulation – maintenance phases, spares, crews
Notes: Weibull, Gumbel, Gamma, Exponential, Normal, Logistic, Arrhenius-Weibull
Fast! 1000 simulations of 4 weeks on 4 yr old Macbook Pro running Vista in Parallels < 4 minutes

## Slide 10: BlockSim 7/8 Model

## Slide 11: Ion Source

## Slide 12: RF Systems

## Slide 13: Standby Containers

## Slide 14: Full Accelerator Simulation Results
Used exponential distributions (random failures)
86% - corrector power supplies, circulators, PPS modules, water valves, JT valves, etc.
Change values for PS controllers and circulators from 50k to 100k
89% - RF feedthroughs, JT valves, etc.
Change RF feedthrough from 100k to 4m (1 every 7 years), JT valves from 87k to 400k (1 every 5 years), etc
92% - Finally! But only for 1 seed

## Slide 15: Klystron Spares Study
805 MHz, 550 (700) kW peak, 50 kW average power, 1.5 ms pulse length, 9% duty cycle
M type cathode, 0.6-0.7 A/cm2 density, manufacturer predicted lifetime > 100,000 hours
81 in service, 70 with ~40000 hours on filament
How many spares to order and how quickly?
Notes: 2.8 million hours total. 6200 hrs operation per year. Efficiency 67%, gain 51 dB. SLAC klystrons – 2856 MHz, 65 MW peak, 41 kW average, 3.5 us gain 50 dB, efficiency 45%, density 8 A/cm^2

## Slide 17: Weibull Distribution Parameters
Beta – “Shape” Parameter
Eta – “Scale” Parameter

## Slide 18: Klystron failures, different values of β
Notes: Assuming we are at 40k hours already

## Slide 19: Klystron failures, different values of η
Notes: Assuming we are at 40k hours already

## Slide 20: Cathode Life Time
Dispenser Cathodes: The Current State of the Technology
  L. R. Falce, Hughs Aircraft Company, Electron Dynamics Division, IEDM 83
B,S
M,CD (Alloy)
MM, SCANDATE

## Slide 21: Conclusions
SNS is middle aged - how long will it last?
We still can not predict the wear-out curve – until it begins! But we can model maintenance plans
Cathode lifetime may not be a major concern
Klystron spares can be ordered at a steady rate