## Slide 1: Automation of Operations at Fermilab
Check lists to mouse clicks
The Fermi National Accelerator Laboratory is a U.S. Department of Energy (DOE) research laboratory, operated under DOE contract by Fermi Research Alliance (LLC), a joint partnership of the University of Chicago and the Universities Research Association (URA).

## Slide 2: Abstract
Implementing system automation to increase productivity, improve efficiency, ensure repeatability, and reduce errors has become essential for complex accelerator operations. This presentation will address some of the positive and negative effects of automation on operations and operators using experiences and examples from the Fermilab Operations Department.

## Slide 3: Overview
Intro
  Machines
  Operational Modes
Automation Examples
  Accelerator Coordination
  Collider
  Anti-Proton
  Neutrino Production
Operations
  Affects
  Pros
  Cons
  Maybes
Summary

## Slide 4: Machine Intro
Proton Source
  Provides 8 GeV protons
Booster Neutrino Beamline (MiniBoone)
  8 GeV protons for neutrino production
Main Injector
  120 GeV proton for fixed target
  120 GeV protons for anti-proton production
  120 GeV protons for neutrino production
  150 GeV protons and anti-protons for collider
  8 GeV anti-protons
Switchyard (Fixed Target)
    120 GeV protons for Test Facility
Anti-Proton Source
  120 GeV protons to target
  8 GeV anti-protons (pbars)
NuMI beamline
  120 GeV protons for neutrino production
Tevatron
  Anti-proton on proton collider
Recycler Ring
  8 GeV anti-proton storage ring
Notes: Proton Source delivers 8 GeV protons to BNB for neutrino production
It also sends 8 GeV protons to the Main Injector.
The Main Injector is the multi-tasker, sending 120 GeV protons to fixed target, anti-proton production (where 8 GeV anti-protons are accumulated), NuMI neutrino production, and 150 GeV protons for the collider. It also tranfers 8 GeV pbar from the Anti-proton source to the Recycler.
The Recycler serves as a large pbar storage before sending them through MI to the Tevatron

## Slide 5: Operational Modes
Collider Store
  ~16 hours
Fixed Target
  Approx. once per minute
Neutrino Production
  NuMI (MINOS, MINERA)
    350 kW ~0.5 Hz
  BNB (MiniBooNE)
    2.5-5 Hz
Anti-Proton Production (Stacking)
  ~0.5 Hz rate
  30 mA ~ 1hr
Anti-Proton Transfer to Recycler (Stashing)
  10 minutes
Tevatron Shot Set Up
  ~ 1 hour
Repeat !
Store
NuMI
BNB
Stack to 30 mA
Pbars in Recycler
Notes: I will present examples of system automation that has evolved at Fermi lab over the past 12 years of operation. In that time we provided proton beam fixed target facility, for neutrino production at two separate neutrino experiments and for anti-proton production (stacking). After 40 min of anti-proton production, the anti-proton source delivered anti-protons to the anti-proton storage ring (stashing). Finally protons are loaded into the tevatron and anti-protons are transferred from the recycler to the tevatron to establish colliding beams.

## Slide 6: Accelerator Coordination
Maximize store hours, minimize shot set up time, don’t waste time transitioning between operational modes, and still deliver beam for neutrinos. The first step was better coordination through automation.
Notes: The numbers that I showed were where we ended up. But to get there required reducing time spent in shot set up, and minimizing the effects of anti-proton transfers on both pbar and neutrino production. As well as changing modes quickly and efficiently. Maximize useful store hours, and keep the other users satisfied (relatively). The first step was better accelerator coordination.

## Slide 7: Accelerator Coordination
Timeline Generator (TLG)
  Sets overall Accelerator Complex timing clock events (TCLK) to orchestrate beam delivery from machine to machine.
  Timelines built with modules
    Allows quick reconfiguration of operational modes
  One-Shot function
    Minimized impact of Shot Set Up and Pbar Transfers on beam delivered for NuMI and Pbar Production
  Sequencer Loading
    Increased efficiency of timeline transition during Shot Set Up and Pbar Transfers
Replaced Operators building individual timelines for mode changes
  Increased efficiency and reduced errors
Protons on NuMI target during Tevatron shot setup
0 0.5 1 1.5 2 2.5
hours
0
1
2
3
4
5
6
7
8
9
10
Protons on target (1016 )
9.07x1016 POT
8.81x1016 POT
6.64x1016 POT
Impact thanks to sequencer and timeline changes
Notes: The TLG gets an overhall.

## Slide 8: Accelerator Coordination
State Devices
  Provide persistent conditions, triggers and informational messages through Accelerator Control Network (ACNET) parameters
  When a state device is set, it is reflected to the rest of the control system
    Multicast
    Registered listeners (Sequencers)
  Sequencer can set state devices
Tevatron States
Recycler States
Notes: State Devices to coordinate

## Slide 9: Accelerator Coordination
“Smarter” Sequencer
  Separate sequencer instances for TeV, MI, Pbar, Recycler
  Sequencer issues high level control commands
    Changes Timeline
    Launch programs and scripts for complex operations (Tev_Auto_Closure)
  Listens too and sets State Devices to provide synchronization
    (V:RRTLG)
  Implemented to improve efficiency of Shot Set Up and Pbar Transfers to Recycler

## Slide 10: Collider Automation
Focus on reducing the shot set up time, and build some tools to be proactive and increase productivity.
Notes: Shot set up

## Slide 11: Collider Automation
Automated Injection Closure program
  Forward and Reverse injection
Tune Tracker (PPLL)
  Provided continuous measurement of Tev tunes during tune up, ramp and squeeze
  Monitor tune drift during the store
    Alarmed when out of tolerance
    Manual Correction
    Improved response time to maintain stable tunes throughout the store
Chromaticity Tracker
  Auto Chromaticity Measurement Program
    Set the chromaticities, and coupling for Tevatron Shot setup

## Slide 12: Collider Automation
Automated Collimators to remove halo at IP
  Beam intensity and loss monitor feedback
  Reduced time from 30 to 10 min.
Orbit Stabilization Program
  Orbit smoothed to a reference orbit file one time at lowbeta, at Int collisions and at the end of a store.
  During a store, corrects the orbit every 30 sec.
  Implemented to correct orbit drift due to environmental factors and corrector failures.
Proton bunched beam intensity
Pbar bunched beam intensity
F49 local BLM
D49 local BLM

## Slide 13: Anti-Proton Automation
Increase the repeatability and consistency of the beam conditions for the anti-protons. Normalize the results with automation.
Notes: Stacking was more of an art before implementing auto tune beam lines and cooling regulation. Unfortunately art is sometimes in the eye of the beholder.

## Slide 14: Anti-Proton Automation
Beam Line Tuner
  120 GeV proton trajectory in 3 beamlines prior to the Pbar target and 8 GeV secondary beam after the target.
    Replaced Operators target tuning.
Stacktail Monitor
  Regulates stacktail momentum cooling power
Core Babysitter
  Core momentum cooling power regulation

## Slide 15: Results
Pbar Transfer
Tevatron Shot Set Up
Notes: Not all due to automation, but it was a contributing factor

## Slide 16: Neutrino Production
With all this collider and pbar production who has time to make neutrinos?
Notes: Collider and pbar did consume sometime

## Slide 17: Neutrino Production
Booster Neutrino Beamline Tuner (MiniBoone)
  Target position stability
    2-5 Hz rate
NuMI Beamline Tuner
  Target position
    100µm rms
    350 kW beam power on target MINOS, MINERA
    700 kW NOA (future)

## Slide 18: Affects on Operators/Operations
What does this button do?
Notes: Collider and pbar did consume sometime

## Slide 19: Affects on Operators/Operations
Process/System knowledge suffers.
  Slows learning.
  A good operator will learn it.
Operations becomes more expert dependent.
  First response is to call someone.
Difficult to operate in a non-standard configuration.
  Large pbar stack sizes.
Requires more attention in training
  Don’t just know that it works, know how it works.
Notes: When you sit down to write a talk about how automation has affected the accelerator operations you can for the most part make a quantitative analysis, but considering it’s affect on the operators knowledge is not even qualitative it’s more of a gut feeling. You can point to general examples that have been observed, but we aren’t in the habit of keep track how long something would take under different circumstances that don’t exist in your system. You perceive a reduction in process knowledge, and you believe that will negatively impact creativity and problem solving skills, but it’s not something that can be determined until it’s tested.
The machine knowledge does declines. It’s hard to learn how to compensate for a bad corrector or identify a quad steering problem if you haven’t spent time tuning.
It stunts the development of trouble shooting skills.

## Slide 20: Affects on Operators/Operations
Increase productivity.
  Focus on areas that have no automation.
Expands our responsibility.
Different skills are being developed
  More computer savvy, operators that write their own automation programs.
  Is this just the evolution of an operator at work?

## Slide 21: Summary
Automation when it’s done correctly improves reliability, reduces human error, increases productivity, and is a necessity for complex operations. Generally the benefits outweigh the drawbacks, and with effort, attention and training Operations can nearly eliminate them.
Notes: Automation when it’s done correctly improves reliability, reduces human error, increases productivity, and is a necessity for complex operations. Generally the benefits outweigh the drawbacks, and with effort, attention and training Operations can nearly eliminate them.

## Slide 22: Summary
Automation
  Improves reliability
  Reduces human error
  Increases accelerator productivity
  Is a necessity for complex operations
Operations/Operators
  Will adjust and evolve

## Slide 23: AUTOMATION
1: the technique of making an apparatus, a process, or a system operate automatically
2: the state of being operated automatically
3: automatically controlled operation of an apparatus, process, or system by mechanical or electronic devices that take the place of human labor

## Slide 24: Thank You.